## Slide 1
Project Motivation and Objectives
Atomic force microscopy (AFM) maps surface topography by scanning a sharp tip across a sample.
  The recorded image mixes sample geometry with tip geometry - tip effects are easy to underestimate and hard to visualize.
Build an interactive browser-based forward simulator of tip-sample interactions via morphological operations.
  Make tip-induced artifacts (broadening, rounding, double-tip ghosts) immediately visible.
  Support reproducible export and a path toward later inverse / ML reconstruction work.
Methods and Approach
Forward Model:
    Contact-mode height-field simulation via Minkowski operations
Dilation:
Erosion
(concave
tips):
Workflow:
Select or import tip geometry
Select or import sample surface
Compute measured height map
Compare true vs measured vs error
Custom Geometry:
Import .OBJ meshes for arbitrary tip/surface shapes
Rasterized to discrete grid for physics computation
Results and Discussion
Visualizing AFM Tip-Sample Artifacts with a Browser-Based Forward Model
Avish Cooray, Soumik Sarkar, Adarsh Krishnamurthy, Alloy Das
Iowa State University
Simulator Controls and Features
Acknowledgements
I would like to thank Dr. Soumik Sarkar, Principal Investigator of the Translational AI Center, for project guidance and mentorship; Dr. Adarsh Krishnamurthy for technical direction and feedback; and Alloy Das for close mentorship and support throughout this work.
Partial funding for this work was provided by a grant from the National Science Foundation (CISE 2447479).
M[i] = max_j { S[i+j] - T[j] }
M[i] = min_j { S[i+j] + T[j] }
2D Line-Scan Simulator
True image
Measured image
3D Raster-Scan Simulator
True image
Measured image
Interactive, browser-based, zero-install
Real-time parameter adjustment: tip shape, surface geometry, noise
Side-by-side true surface vs. measured image vs. per-pixel error map
Import/export: .OBJ meshes, CSV height maps, 16-bit PNG, JSON parameters
Python forward model (afm_forward_model.py) for batch simulation and validation
Ask for Demo!
8 tip geometries + custom (.OBJ):
  sphere, cone, sphere-cone, hyperboloid, flat punch, asymmetric, double-tip, concave sphere + custom (.OBJ)
10 surface types + custom (.OBJ):
  sinusoidal, rolling hills, nanoparticle, nano-pit, trench, rough, pyramid, DNA ridges, chirp, lattice
Invert controls: Mirror X/Y and invert Z controls for exploring surface orientation and sign conventions.
Erosion toggle: switch from dilation to erosion to visualize the inverse operation
Noise injection: add measurement noise to explore robustness
Export panel: CSV, PNG, JSON, .OBJ with one click
References
1 J.S. Villarrubia, "Algorithms for Scanned Probe Microscope Image Simulation, Surface Reconstruction, and Tip Estimation," J. Res. Natl. Inst. Stand. Technol., vol. 102, no. 4, pp. 425-454, 1997.
2 D. Necas and P. Klapetek, "Gwyddion: An open-source software for SPM data analysis," Cent. Eur. J. Phys., vol. 10, no. 1, pp. 181-188, 2012.
3 P. Hachenberger, "3D Minkowski Sum of Polyhedra," in CGAL User and Reference Manual, CGAL Editorial Board, v6.2, 2024.
Future Work
Import real .spm height maps for validation
Generate labeled synthetic datasets in batch
Develop ML-based inverse reconstruction of surface and tip geometry